## Slide 1: Computer Architecture Branch Prediction
By Yoav Etsion and Dan Tsafrir Presentation based on slides by David Patterson, Avi Mendelson, Lihu Rappoport, and Adi Yoaz

## Slide 2: Pipelined CPU with Control
ALUSrc
6
ALU
result
Zero
Add
result
Add
Shift
left 2
ALU
Control
ALUOp
RegDst
RegWrite
Read
reg 1
Read
reg 2
Write
reg
Write
data
Read
data 1
Read
data 2
Register File
[15-0]
[20-16]
[15-11]
Sign
extend
16
32
ID/EX
EX/MEM
MEM/WB
Instruction
MemRead
MemWrite
Address
Write
Data
Read
Data
Data
Memory
Branch
PCSrc
MemtoReg
4
Instruction
Memory
Address
Add
IF/ID
PC
0
1
m
u
x
0
1
m
u
x
0
1
m
u
x
0
1
m
u
x
Instruction
Control
WB
MEM
WB
MEM
WB
EXE
Instruction
Decode /
register fetch
Instruction
fetch
Execute /
address
calculation
Memory
access
Write
back
Notes: Of course, in the previous diagrams, we didn’t see the actual control; we just assumed it’s there
The control is responsible to run the 5 stages together in a valid manner

## Slide 3: Pipeline Hazards: 1. Structural Hazards

## Slide 4: Pipeline Hazards: 2. Data Hazards

## Slide 5: Pipeline Hazards: 3. Control Hazards

## Slide 6: Branch, but where?
The decision to branch happens deep within the pipeline
Likewise, the target of the branch becomes known deep within the pipeline
How does this affect the pipeline logic?
For example…

## Slide 7
Executing a BEQ Instruction
BEQ R4, R5, 27 → if (R4-R5=0) then PC  PC+4+SignExt(27)*4 ;
else PC  PC+4
0 or
4 beq R4, R5, 27 8 and 12 sw
16 sub
ALUSrc
6
ALU
result
Zero
Add
result
Add
Shift
left 2
ALU
Control
ALUOp
RegDst
RegWrite
Read
reg 1
Read
reg 2
Write
reg
Write
data
Read
data 1
Read
data 2
Register File
[15-0]
[20-16]
[15-11]
Sign
extend
16
32
ID/EX
EX/MEM
MEM/WB
Instruction
MemRead
MemWrite
Address
Write
Data
Read
Data
Data
Memory
Branch
PCSrc
MemtoReg
4
Instruction
Memory
Address
Add
IF/ID
PC
0
1
m
u
x
0
1
m
u
x
0
1
m
u
x
0
1
m
u
x
Instruction
R4-R5=0
-
8+SignExt(27)*4
12
16
16
beq
and
sw
…Now we know, but only in next cycle will this effect PC
Calculate branch condition = compute R4-R5 & compare to 0
Calculate branch target
Notes: Read this slide left to right

## Slide 8: Control Hazard on Branches
And
Beq
sub
sw
Inst from target
I
M
R
e
g
D
M
R
e
g
PC
I
M
R
e
g
D
M
R
e
g
PC
I
M
R
e
g
D
M
R
e
g
PC
I
M
R
e
g
D
M
R
e
g
PC
I
M
R
e
g
D
M
R
e
g
PC
Outcome: The 3 instructions following the branch are in the pipeline even if
branch is taken!

## Slide 9: Stall
Easiest solution:
  Stall pipe when branch encountered until resolved
But there’s a prices. Assume:
  CPI = 1
  20% of instructions are branches (realistic)
  Stall 3 cycles on every branch (extra 3 cycles for each branch)
Then the price is:
  [ CPI new = CPI Ideal + avg. stall cycles / instr. ]
  CPI new = 1 + 0.2 × 3 = 1.6 // 1 = all instr., including branch
Namely:
  IPC drops from 1 to 1/1.6
  We lose ~37% of the performance!
And modern pipelines are typically longer…

## Slide 10: What do we do on branches?
Speculative execution
  Speculate on branch outcome to continue fetching
  Flush pipeline on mispredictions
One option: Static prediction
  E.g., all branches as taken
  Simplistic assumption: 50% hit rate
  CPI new = 1 + (0.2 × 0.5) × 3 = 1.3
  23% slowdown instead of 37%
  Simple, but success is likely > 50%...
Better option: Dynamic prediction
  Learn the workload at run time

## Slide 11: Traps, Exceptions and Interrupts
Indication of events that require a higher authority to intervene (i.e. the operating system)
Atomically changes the protection mode and branches to OS
  Protection mode determines what the running is allowed to do (access devices, memory, etc).
Traps: Synchronous
  The program asks for OS services (e.g. access a device)
Exceptions: Synchronous
  The program did something bad (divide-by-zero; prot. violation)
Interrupts: Asynchronous
  An external device needs OS attention (finished an operation)
Can these be handled like regular branches?
Notes: Interrupts may occur at any stage in the pipeline
You will learn more in the OS course

## Slide 12: What do we need to speculate on?
Given an instruction, need to predict if it’s a branch and…
  Branch type, namely determine if the branch is
    Conditional / unconditional; direct / indirect; call / return / other
  For conditional branch, need to determine “direction”
    Direction mean: “taken” or “not taken”
    Actual direction is known only after execution
    Wrong direction prediction => pipeline flush
  For taken branch (cond. on uncond.), need to determine “target”
    Target of direct branches known at decode
    Target of indirect branches known at execution
Goal
  Minimize branch misprediction rate (for a given predictor size)

## Slide 13: At Fetch: Branch Target Buffer
fast lookup table
PC of fetched instruction
?=
Predicted branch
taken or not taken? (last few times)
No => we don’t know, so we don’t predict
Yes => instruction is a branch, so let’s predict it
Branch PC Target PC History
Predicted
Target
(Works in a straightforward manner only for direct branches, otherwise target PC changes)
Notes: Read left to right.
Works only for direct branches (MIPS has an indirect branch instructions, e.g., jal and jmp; note they are unconditional = always taken)

## Slide 14: How it works in a nutshell
Until proven otherwise, assume branches are not taken
  Fall through instructions (assume branch has no effect)
Upon the first time a branch is taken
  Pay the price (in terms of stalls), but
  Save the details of the branch in the BTB (= PC, target PC, and whether or not branch was taken)
While fetching, HW checks in parallel
  Whether PC is in BTB
If found, make a prediction
  Taken? Address?
Upon misprediction
  Flush (throw out) pipeline content & start over from right PC

## Slide 15: Using The BTB
PC moves to next instruction
Inst Mem gets PC
and fetches new inst
BTB gets PC
and looks it up
IF/ID reg. loaded
with new inst
BTB Hit ?
Br taken ?
PC  PC + 4
PC  pred addr
IF
ID
IF/ID reg. loaded
with pred inst
IF/ID reg. loaded
with seq. inst
Branch ?
yes
no
no
yes
no
yes
EXE

## Slide 16: Using The BTB (cont.)
ID
EXE
MEM
WB
Branch ?
Calculate br
cond & trgt
Flush pipe &
update PC
Corect
pred ?
yes
no
IF/ID latch loaded
with correct inst
continue
Update BTB
yes
no
continue

## Slide 17: What/Who/When We Predict/Fix
Fetch [BTB]
Decode
Execute
Target Array
Branch type
  conditional
  unconditional direct
  unconditional indirect
  call
  return
Branch target
Return Stack Buffer
Predict return target
Cond. Branch Predictor
Predict conditional T/NT
Fix wrong (direct) target for uncond. branches
Fix wrong targets for (direct) cond. branches that were predicted taken
on direction miss
try to fix
Fix TA miss
Fix Wrong prediction
Fix Wrong prediction
Dec Flush
Exe Flush

## Slide 18: Branches and Performance
MPI : misprediction-per-instruction:
# of incorrectly predicted branches
MPI =
total # of instructions
How is this different from misprediction rate?
  The number of branch instructions in the code is highly workload-specific
  MPI takes the rate of branches into account

## Slide 19: Branches and Performance
MPI : misprediction-per-instruction:
# of incorrectly predicted branches
MPI =
total # of instructions
MPI correlates well with performance. For example:
  MPI = 1% (1 out of 100 instructions @1 out of 20 branches)
  Ideal IPC=2; flush penalty of 10 cycles
We get:
  MPI = 1%  flush in every 100 instructions
  Since IPC=2, we have 1 flush every 50 cycles
  10 cycles flush penalty every 50 cycles
  20% in performance

## Slide 20: Predicting Direction of Conditional Branch: “Taken” or “Not Taken”?

## Slide 21: One-Bit Predictor
One problem with 1-bit predictor:
  Double-mistake in loops
  Branch Outcome 1 1 1 1 1 0 1 1 1 1 1 0 1 1 1 1 1 1
  Prediction ? 1 1 1 1 1 0 1 1 1 1 1 0 1 1 1 1 1
branch IP (actually, some of is lsb-s)
Prediction (at fetch):
previous branch outcome
counter array / cache
Update (at execution)
Update bit width
branch outcome

## Slide 22: Bimodal (2-bit) Predictor
A 2-bit saturating counter avoids the double mistake in glitches
  Need “more evidence” to change prediction
2 bits encode one of 4 states
  00 – strong NT, 01 – weakly NT, 10 – weakly taken, 11 – strong taken
  Commonly initialized to “weakly-*”
Update
  Branch was actually taken: increment counter (saturate at 11)
  Branch was actually not-taken: decrement counter (saturate at 00)
Predict according to MSB of counter (0 = NT, 1 = taken)
00
SNT
taken
not-taken
taken
taken
taken
not-taken
not-taken
not-
taken
01
WNT
10
WT
11
ST
Predict taken
Predict not-taken

## Slide 23: Bimodal Predictor (cont.)
lsb-s of branch IP
Prediction = MSB of counter
array of 2-bit saturating counters
Update counter with
branch outcome ++ if taken
-- if not take (avoid overflowing)
Problem:
Doesn’t predict well with patterns like 010101… (see example next slide)

## Slide 24: Bimodal Predictor - example
Br1 prediction
  Pattern: 1 0 1 0 1 0
  counter: 2 3 2 3 2 3
  Prediction: T T T T T T
Br2 prediction
  Pattern: 0 1 0 1 0 1
  counter: 2 1 2 1 2 1
  Prediction: T nT T nT T nT
Br3 prediction
  Pattern: 1 1 1 1 1 0
  counter: 2 3 3 3 3 3
  Prediction: T T T T T T
Code:
Loop: ….
br1: if (n/2) {
/*odd*/ ……. }
br2: if ((n+1)/2) {
/*even*/ ……. }
n--
br3: JNZ n, Loop
Notes: Assume counter is initialized to 2 in all cases

## Slide 25: 2-level predictors
More advanced branch predictors work in 2 levels
There are local predictors
  A branch B can be predicted based on past behavior of B
And global predictors
  B is mostly affected by nearby branches

## Slide 26: Local Predictor
Save the history of each branch in a Branch History Register (BHR):
  Shift-register updated by branch outcome (new bit in => oldest bit out)
  Saves the last n outcomes of the branch
  Used as a pointer to an array of bits specifying direction per history
Example: assume n=6
  Assume the pattern 000100010001 . . .
  At the steady-state, the following patterns are repeated in the BHR:
000100010001 . . .
000100
001000
010001
100010
Following 000100, 010001, 100010 the jump is not taken
Following 001000 the jump is taken
BHR
0
2n-1
n

## Slide 27: Local Predictor (2nd level)
Like before, there could be glitches from the pattern
  Use 2-bit saturating counters instead of 1 bit to record outcome:
Too long BHRs are not good:
  Distant past history may no longer be relevant
  Warm-up is longer
  Counter array becomes too big (2^n)
Update
History
with
branch
outcome
prediction =
msb of counter
2-bit-sat counter array
Update counter with
branch outcome ++ if taken; -- otherwise
history
BHR

## Slide 28: Local Predictor: private counter arrays
Branch IP
tag
history BHR
prediction =
msb of counter
2-bit-sat counter arrays
update counter with
branch outcome
update
history
pattern with
branch
outcome
history cache
Predictor size: #BHRs × (tag_size + history_size + 2 × 2 history_size)
Example: #BHRs = 1024; tag_size=8; history_size=6 
size=1024 × (8 + 6 + 2×26) = 142Kbit (too big)
Holding BHRs and counter arrays for many branches:
counter size X counter#

## Slide 29: Reducing size: shared counter arrays
Using a single counter array shared by all BHR entries
  All BHRs index the same array (2nd level is shared)
  Branches with identical history interfere with each other (though, empirically, it still works reasonably well)
prediction =
msb of counter
Branch IP
2-bit-sat counter array
tag
history1
history cache
Predictor size: #BHRs × (tag_size + history_size) + 2 × 2 history_size
Example: #BHRs = 1024; tag_size=8; history_size=6 
size=1024 × (8 + 6) + 2×26 = 14.1Kbit (much smaller)
tag
history2

## Slide 30: Local Predictor: lselect
lselect reduces inter-branch-interference in the counter array by concatenating some IP bits to the BHRs, thereby making the counter array longer
prediction =
msb of counter
Branch IP
2-bit-sat counter array
tag
history
history cache
h
h+m bits
Next m LSBs of IP
Predictor size: #BHRs × (tag_size + history_size) + 2 × 2 history_size + m => the 2bit array is 2^m bigger (overall, a small addition for small m)

## Slide 31: Local Predictor: lshare
lshare reduces inter-branch-interference in the counter array with XOR:
(maps common patterns of different branches to different counters)
h
h
Next h LSBs of IP
history cache
tag
history
prediction =
msb of counter
Branch IP
2-bit-sat counter array
Predictor size: #BHRs × (tag_size + history_size) + 2 × 2 history_size

## Slide 32: Global Predictor
Sometimes, a branch’s behavior tightly correlates with that of other branches:
if (x < 1) . . .
if (x > 1) . . .
Using a Global History Register (GHR), the prediction of the second if may be based on the direction of the first if
  Used for all conditional branches
Yet, for other branches such history “interference” might be destructive
  To compensate, need long history

## Slide 33: Global Predictor (cont.)
update
history
with
branch
outcome
prediction =
msb of counter
2-bit-sat counter array
update counter with
branch outcome
history
GHR
The predictor size: history_size + 2*2 history_size
Example: history_size = 12  size = 8 K Bits

## Slide 34: Global Predictor: Gshare
gshare combines the global history information with the branch IP using XOR (again, maps common patterns of different branches to different counters)
prediction =
msb of counter
2-bit-sat counter array
update counter with
branch outcome
Branch IP
history
GHR
update
history
with
branch
outcome

## Slide 35: Hybrid (Tournament) Predictor
Note: the chooser array may also be indexed by the GHR
++ if Bimodal / Local correct and Global wrong
-- if Bimodal / Local wrong and Global correct
Bimodal /
Local
Global
Branch IP
Prediction
Chooser array (an array
of 2-bit sat. counters)
GHR
A tournament predictor dynamically selects between 2 predictors:
  Use the predictor with better prediction record (example: Alpha 21264)

## Slide 36: Speculative History Updates
Deep pipeline  many cycles between fetch and branch resolution
  If history is updated only at resolution
    Local: future occurrences of the same branch may see stale history
    Global: future occurrences of all branches may see stale history
  History is speculatively updated according to the prediction
    History must be corrected if the branch is mispredicted
    Speculative updates are done in a special field to enable recovery
Speculative history update
  Speculative history updated assuming previous predictions are correct
  Speculation bit set to indicate that speculative history is used
  As usual, counter array updated only when outcome is known (that is, it is not updated speculatively)
On branch resolution
  Update the real history (needed only for misprediction) and counters

## Slide 37: “Return” Stack Buffer
A return instruction is a special case of an indirect branch:
  Each time jumps to a potentially different target
  Target is determined by the location of the corresponding call instruction
The idea:
  Hold a small stack of targets
  When the target array predicts a call
    Push the address of the instruction which follows the call-instuction into the stack
  When the target array predicts a return
    Pop a target from the stack and use it as the return address

## Slide 38: Branch Prediction in commercial Processors

## Slide 39: Real World Predictors
386 / 486
  All branches are statically predicted “Not Taken”
Pentium
  IP based, 2-bit saturating counters (Lee-Smith)
    An array indexed by part of IP bits
  Upon predictor miss (IP not in found in array)
    Statically predicted “not taken”

## Slide 40: Intel Pentium III
2-level, local histories, per-set counters
4-way set associative: 512 entries in 128 sets
IP
Tag
Hist
1001
Pred=
msb of
counter
9
0
15
Way 0
Way 1
Target
Way 2
Way 3
9
4
32
counters
128
sets
P
T
V
2
1
1
32
LRR
2
Per-Set
Branch Type
00- cond
01- ret
10- call
11- uncond
Return
Stack
Buffer

## Slide 41: Alpha 21264 - LG Tournament
1024
3
Counters
4 ways
256
Histories
IP
In each entry:
6 bit tag +
10 bit History
4096
2
Counters
GHR
12
4096
Counters
M
X
U
Global
Local
Chooser
2
New entry on the Local stage is allocated on a global stage miss-prediction
Chooser state-machines: 2 bit each:
  one bit saves last time global correct/wrong,
  and the other bit saves for the local correct/wrong
Chooses Local only if local was correct and global was wrong

## Slide 42: Pentium® M
Combines 3 predictors
  Bimodal, Global and Loop predictor
Loop predictor analyzes branches to see if they have loop behavior
  Moving in one direction (taken or NT) a fixed number of times
  Ended with a single movement in the opposite direction

## Slide 43: Pentium® M – Indirect Branch Predictor
Indirect branch targets is data dependent
  Can have many targets: e.g., a case statement
  Can still have only a single target at run time
  Resolved at execution  high misprediction penalty
Used in object-oriented code (C++, Java)
  becomes a growing source of branch mispredictions
A dedicated indirect branch target predictor (iBTB)
  Chooses targets based on a global history (similar to global predictor)
Initially indirect branch is allocated only in the BTB
  If target is mispredicted  allocate an iBTB entry corresponding to the global history leading to this instance of the indirect branch
  Data-dependent indirect branches allocate as many targets as needed
  Monotonic indirect branches are still predicted by the TA

## Slide 44: Indirect branch target prediction (cont)
Prediction from the iBTB is used if
  BTB indicates an indirect branch
  iBTB hits for the current global history (XORed with branch address)
BTB
iBTB
Branch IP
Predicted
Target
M
X
U
hit
indirect branch
hit
Target
HIT
Global history
Target

## Slide 45: Summary
Branches are frequent
Branches are bad (for performance)
Branches are mostly predictable…
Speculating branch outcome improve pipeline utilization
Speculation better be accurate:
  Remember the example: a single mispredicted branch per 100 instructions can reduce performance by 20% (IPC=2)
It is effective to spend a lot of transistors on branch predictors
  Prediction accuracy is typically over 96%